## Slide 1: DA1469x AoA Demo Assembly Instructions
July 29, 2019
V1.0

## Slide 2: Current AoA Demo
YouTube link: https://www.youtube.com/watch?v=jSDtUOQXJmo
Receiver
Transmitter

## Slide 3: AoA Demo Assembly
You may have received Dialog DA1469x development kit and Antenna boards separately from Dialog.
The instructions in this document will allow you to assemble them so that you can reproduce the demo as shown in the YouTube video in the previous slide.
Objective

## Slide 4: AoA Demo Components
Receiver
  One 69x pro-kit motherboard, +
  69x AoA daughter card plugged in, +
  LCD board (Although there is console output with AoA data, the LCD makes it more meaningful)
Transmitter
  One 69x USB dongle
LCD
  Part number is Adafruit1651 (https://www.mouser.com/ProductDetail/Adafruit/1651?qs=%2Fha2pyFadui%252ByqmMEPPjygZK5phD6F9p2KQ2m%2FKMX2M%3D )
Adding the LCD to DA1469x motherboard will require couple of small reworks.
Hardware Components

## Slide 5: Connecting the LCD board
  DA1469x Pro-Kit development kit comes with a motherboard and 69x daughter card.
  The rework instructions are for Rev C of the board
  Put aside the 69x daughter board
  Just take the motherboard

## Slide 6: Connecting the LCD board
Remove R305, and put it at R307
Install Sockets: J11, J12, J13, J14
Note:
  In this configuration the motherboard needs to be
  connected to a pc/laptop using USB mini cable.
DA1469x ProKit Motherboard Schematic
  https://www.dialog-semiconductor.com/sites/default/files/da14695-mb-pro_vc-sch.pdf
DA1469x ProKit Documentation:
  https://www.dialog-semiconductor.com/products/da14695-development-kit-pro

## Slide 7: Putting it together
Plug in the AoA daughter card to mother board
Plug in the LCD display to the sockets just installed.
Connect the motherboard to a pc/laptop using a USB mini cable
Now we are ready to program the flash
Assembly

## Slide 8: AoA Demo Software
For AoA demo, we currently share the binary images only, no source code provided.
Please note that this is a separate code base from ToF demo.
It is expected that the customer has
  Registered on Dialog website,
  Downloaded and installed SmartSnippets Studio and the latest SDK
    https://www.dialog-semiconductor.com/products/da1469x-product-family

## Slide 9: AoA Demo Software Programming
AoA demo software is provided in binary format. Files are shared via ftp site as communicated via email
Download and unzip the files. Review file readme.md. It has instructions for flash programming. Edit the flash programming command lines to suit your pc environment.
Receiver programming:
  The AoA antenna board with DA1469x may already be programmed with AoA software.
  If not, execute the scripts to program the Receiver (Sample log attached)
Transmitter programming
  Execute the scripts to program the receiver (69x USB dongle)
  Sample log attached
Reset both transmitter and receiver boards. Demo should be ready
Flash Programming

## Slide 10: Thank You !